## Slide 1: Master Thesis Project: Bending-Twist Shape Adaptation of Wings by Compliant Chiral Spar Design
Alejandro Valverde López, Cranfield University
Advisors: Runkel, Falk; Keidel, Dominic; Urban Fasel

## Slide 2: Motivation
Gust alleviation
Wing demonstrator
Raither(2013)

## Slide 3: Different approaches
Working principle, publicated on: Raither(2013)
Runkel (2015): Δβ → material anisotropy
ΔT → G2 t2
Current project: Buckling-induced shear modulus variation
Notes: Working principle
The variable shear stiffness G2t2 that is required for the activation of the adaptive web can in principle be achieved by changing either the web’s shear modulus or its thickness. The change in shear stiffness of the adaptive web will lead to a shift of the shear center in horizontal direction and thus to a non-zero twist of the profile.
Case 1-Raither:
An implementation based on the variation of the elastic modulus of a polymer web due to changes in temperature is investigated.
Case 2-Runkel:
A particular material anisotropy by varying fibre orientation and thickness of the component is introduced.
Case 3-Chiral:
At a particular external load, the shear flow in the web exceeds the buckling limit, resulting in a drastic reduction of the effective shear modulus of this structural element

## Slide 4: Model overview
Abaqus model with mesh
Script developed in Python
Fully parameterized
Parameter study, with 5 variable parameters
  C-box thickness
  Rib thickness
  Rib frame width
  Chiral ligament eccentricity
  Chiral section thickness
Length in the spanwise dimension: 1.5m
Fixed support at the wing root
Single load at the wing tip

## Slide 5: Preliminary results from simulations
Abaqus Standard Analysis
Displacement imposed at the free extreme
Computation time: 2-5min

## Slide 6: Preliminary results from parametric study
Results evaluated by:
  Initial stiffness of the structure K
  Rotational displacement UR1 along the spanwise direction

## Slide 7: Next steps
This week and upcoming week:
  Finish parametric study
Until the end of the month:
  Start manufacturing demostrator
Gantt chart

## Slide 8: Thank you for your attention!
Bibliography:
W. Raither, M. Heymanns, A. Bergamini, and P. Ermanni, “Morphing wing structure with controllable twist based on adaptive bending twist coupling,” Smart Mater. Struct., vol. 22, no. 6, p. 065017, Jun. 2013.
F. Runkel, A. Arrieta, P. Ermanni, "Design of passive morphing wing structures using elastic instabilities", Proceedings of the 20th International Conference on Composite Materials, p. 1-12, Jul. 2015
D. Bornego, F. Scarpa, C. Remillat, "Evaluation of hexagonal chiral structure for morphing airfoil concept", Proceedings of the Institution of Mechanical Engineers, Part G: Journal of Aerospace Engineering, p. 185--192, vol. 219, no. 3, 2005