## Slide 1: Master Thesis Project: Bending-Twist Shape Adaptation of Wings by Compliant Chiral Spar Design
Alejandro Valverde López, Cranfield University
Advisors: Runkel, Falk; Keidel, Dominic; Urban Fasel

## Slide 2: Motivation
Gust alleviation
Wing demonstrator
Raither(2013)

## Slide 3: Different approaches
Working principle, publicated on: Raither(2013)
Runkel (2015): Δβ → material anisotropy
ΔT → G2 t2
Current project: Buckling-induced shear modulus variation
Fig X: Working principle, Raither (2013)
Fig X: Time-variable lamination in laminate composite shells, Raither (2012)
Fig X: Time-variable lamination in laminate composite shells, Raither (2012)
Fig X: Chiral structures in lattice
Notes: Working principle
The variable shear stiffness G2t2 that is required for the activation of the adaptive web can in principle be achieved by changing either the web’s shear modulus or its thickness. The change in shear stiffness of the adaptive web will lead to a shift of the shear center in horizontal direction and thus to a non-zero twist of the profile.
Case 1-Raither:
An implementation based on the variation of the elastic modulus of a polymer web due to changes in temperature is investigated.
Case 2-Runkel:
A particular material anisotropy by varying fibre orientation and thickness of the component is introduced.
Case 3-Chiral:
At a particular external load, the shear flow in the web exceeds the buckling limit, resulting in a drastic reduction of the effective shear modulus of this structural element

## Slide 4: Working principle for the proposed technology
Elastic instabilities induced on the chiral elements ligaments
Fig X: Set of chiral ligaments undergoing elastic instabilities at the root of the wing-box
Fig X: Compression load test on a basic triangular chiral structure
Reduction of the overall shear modulus G2 for the lattice of chiral structures
Effectively an effective shear modulus G2,eff is introduced
G2,eff <G1

## Slide 5: Analytical model
Used to provide fast insight of the role of each of the design parameters on the final mechanical properties of the beam
Fig X: Analytical model of the closed section beam
Bending deformation provided by Bernoulli-Euler equation:
Specific twist due to torsion provided by St. Venant equation:
Torsional stiffness:

## Slide 6: Computational model
The structure response was obtained executing nonlinear simulations on Abaqus CAE
Program using Python scripting
Fig X: General assembly of the computational model
Fig X: Flow chart showing the execution of the parametric study python code

## Slide 7: Computational model
Chiral structure description
Parameters used in the chiral structure lattice

## Slide 8: Computational model
Wing-box in C-profile and ribs
Parameters used in the wing-box in C-profile design
Parameters used in the ribs design

## Slide 9: Computational model
Chiral lattice nodes rigid modeling
Fig X: Chiral nodes on the manufactured demonstrator
Fig X: Tyre embedded into the lattice chiral node
Lattice nodes are only constraint in rotation around its one axis by the lattice ligaments
In the modelling, they are assumed to behave like rigid bodies

## Slide 10: Computational model
Computational mesh description
Fine mesh size, typically equal to 3 mm.
Course mesh size, typically equal to 30 mm
Fig X:Different mesh regions

## Slide 11: Computational model
Load introduction and boundary condition
Fig X: Fixed boundary condition
Fig X: Load introduction points

## Slide 12: Model analysis
Artificial static energy dissipation using constant damping factor (c)
Fig X: For c = 10-6
Fig X: For c = 10-9
Fig X: Displacement-force curve for various values of constant damping factor c

## Slide 13: References
W. Raither, A. Bergamini, F. Gandhi, and P. Ermanni, “Adaptive bending-twist coupling in laminated composite plates by controllable shear stress transfer,” in Composites Part A: Applied Science and Manufacturing, vol. 43, pp. 1709–1716, 2012.
W. Raither, A. Bergamini, and P. Ermanni, “Profile beams with adaptive bending-twist coupling by adjustable shear centre location,” Journal of Intelligent Material Systems and Structures, vol. 24, no. 3, pp. 334–346, 2013.
G. Ramstein, Experimental Validation of Chiral Structures with Local Controlled Instabilities. Semester project no. 16-015, ETH Zürich, 2016.