## Slide 1
Master Thesis Project Bending-Twist Shape Adaptation of Wings by Compliant Chiral Spar Design
Alejandro Valverde López
Cranfield University
ETH Zürich
07.07.2017 Ostfalia University

## Slide 2
Motivation
Gust alleviation
Wing demonstrator

## Slide 3
Different approaches
Working principle, publicated on: Raither(2013)
Runkel (2015): Δβ → material anisotropy
ΔT → G2 t2
Current project: Buckling-induced shear modulus variation
Notes: Working principle
The variable shear stiffness G2t2 that is required for the activation of the adaptive web can in principle be achieved by changing either the web’s shear modulus or its thickness. The change in shear stiffness of the adaptive web will lead to a shift of the shear center in horizontal direction and thus to a non-zero twist of the profile.
Case 1-Raither:
An implementation based on the variation of the elastic modulus of a polymer web due to changes in temperature is investigated.
Case 2-Runkel:
A particular material anisotropy by varying fibre orientation and thickness of the component is introduced.
Case 3-Chiral:
At a particular external load, the shear flow in the web exceeds the buckling limit, resulting in a drastic reduction of the effective shear modulus of this structural element

## Slide 4
Chiral reticular structure
Constitutive elements
Prall (1997)

## Slide 5
Analytical model
Bending:
St. Venant torsion:

## Slide 6
Wing box model overview
Abaqus model with mesh
Script developed in Python
Fully parameterized
Parameter study, with 5 variable parameters
  C-box thickness
  Rib thickness
  Rib frame width
  Chiral ligament eccentricity
  Chiral section thickness
Length in the spanwise dimension: 1m
Fixed support at the wing root
Various load introduction strategies

## Slide 7
Wing box nonlinear simulations results
Single load introduction point on last rib

## Slide 8
Wing box nonlinear simulations results
Multiple load introduction points on inner ribs

## Slide 9
Wing box nonlinear simulations results
Beam twist evolution with the fraction of load applied

## Slide 10
Whole wing model
Embeded wing box with chiral structure in one of the web
Aerodynamic loads calculated using XFOIL and lift line evalution
FEM + XFOIL interection within a loop until convergence is achieved

## Slide 11
Project status
Analytical model and parametric study
Python code to build the model on Abaqus, fully parameterized
Nonlinear simulation of the wing box model
Done
Nonlinear simulations on the full wing model
Parametric study
To be completed

## Slide 12
Thank you for your attention!
Bibliography:
W. Raither, M. Heymanns, A. Bergamini, and P. Ermanni, “Morphing wing structure with controllable twist based on adaptive bending twist coupling,” Smart Mater. Struct., vol. 22, no. 6, p. 065017, Jun. 2013.
F. Runkel, A. Arrieta, P. Ermanni, "Design of passive morphing wing structures using elastic instabilities", Proceedings of the 20th International Conference on Composite Materials, p. 1-12, Jul. 2015
D. Bornego, F. Scarpa, C. Remillat, "Evaluation of hexagonal chiral structure for morphing airfoil concept", Proceedings of the Institution of Mechanical Engineers, Part G: Journal of Aerospace Engineering, p. 185--192, vol. 219, no. 3, 2005